## Slide 1
FUNDAMENTALS of ENGINEERING SEISMOLOGY
EARTHQUAKE MAGNITUDES

## Slide 2: Earthquake source characterization
Magnitude
Fault dimensions (covered before)
Slip distribution (kinematics)
Fourier transform refresher
Point source representation
  Spectral shape
  Corner frequency
  Stress parameter

## Slide 3: Earthquake Magnitude
Earthquake magnitude scales originated because of
  the desire for an objective measure of earthquake size
  Technological advances -> seismometers

## Slide 4: Earthquake Magnitudes
In the 1930’s, Wadati in Japan and Richter in California noticed that although the peak amplitudes on seismograms from different events differed, the peak amplitudes decreased with distance in a similar manner for different quakes.

## Slide 5
Seismogram Peak Amplitude
The peak amplitude is the size of the largest deflection from the zero line.

## Slide 6
Richter’s Observations

## Slide 7
Richter’s Local Magnitude
Richter used these observations to construct the first magnitude scale, ML (Richter’s Local Magnitude for Southern California).
He based his formula for calculating the magnitude on the astronomical brightness scale - which was logarithmic.

## Slide 8
Logarithmic Scales
In a logarithmic scale such as magnitude
  A change in one magnitude unit means a change of a factor of 10 in the amplitude of ground shaking (wait! This is an often used statement, but it is too simplistic, and I hope you will know why by the end of the course).

## Slide 9
In a logarithmic scale such as magnitude:
  A change in one magnitude unit means a change of a factor of 10 in the amplitude of motion that defines the magnitude. This could be the response of a particular type of instrument, or it could be ground motions at very long periods or ground motions at periods near 1 sec, etc.
  For peak ground motions and response spectra, the scaling is usually less than 10M/2 where M is the moment magnitude, defined shortly, rather than 10M.
The proper statement

## Slide 10: Richter’s Magnitude Scale
Defined for specific attenuation conditions valid for southern California
Only valid for one specific type of seismometer
Can be used elsewhere if local attenuation correction is used and simulated Wood-Anderson response is computed
Not often used now, although it IS a measure of ground shaking at frequencies of engineering interest

## Slide 11
Richter tied his formula to a specific instrument, the Wood-Anderson
torsion seismograph
He assumed a reference motion at a reference distance. To compute the
magnitude at different distances, he calibrated the attenuation function

## Slide 12
Ml=Log Amax -Log A0
-logA0 changes from region to region. The calibration of a local magnitude scale for a given region implies the determination of the empirical attenuation correction for that region (and the magnitude station corrections)
The W-A seismometers are not still used. The W-A recording is computed numerically (by convolving the ground displacement with the W-A transfer function)
Richter fixed the scale assuming that a ML=3 earthquake produces 1mm of maximum amplitude on a Wood-Anderson seismometer at 100 km

## Slide 13
In many studies, the attenuation function is determined by a parametric
approach
where the reference distance and the reference magnitude are fixed
In agreement with the Richter scale.

## Slide 15
In contrast to the general magnitude formula, ML considers only the maximum displacement amplitudes but not their periods. Reason: WA instruments are short-period and their traditional analog recorders had a limited paper speed. Proper reading of the period of high-frequency waves from local events was rather difficult. It was assumed, therefore, that the maximum amplitude phase (which in the case of local events generally corresponds to Sg, Lg or Rg) always had roughly the same dominant period.
The smallest events recorded in local microearthquake studies have negative values of ML while the largest ML is about 7 , i.e., the ML scale also suffers saturation (see later). Despite these limitations, ML estimates of earthquake size are relevant for earthquake engineers and risk assessment since they are closely related to earthquake damage. The main reason is that many structures have natural periods close to that of the WA seismometer (0.8s) or are within the range of its pass-band (about 0.1 - 1 s).
A review of the development and use of the Richter scale for determining earthquake source parameters is given by Boore (1989).
From the IASPEI New Manual Seismological Observatory Practice

## Slide 16: Modern Seismic Magnitudes
Today seismologists use different seismic waves to compute magnitudes
These waves generally have lower frequencies than those used by Richter
These waves are generally recorded at distances of 1000s of kilometers instead of the 100s of kilometers for the Richter scale (this is important because most earthquakes occur in remote places, such as under the oceans, without instruments within 100s of kilometers)

## Slide 17
Teleseismic MS and mb
Two commonly used modern magnitude scales are:
    MS, Surface-wave magnitude (Rayleigh Wave)
    mb, Body-wave magnitude (P-wave)

## Slide 18
Note: also Ms suffers of saturation (see later…)
Collaboration between research teams in Prague, Moscow and Sofia resulted in the proposal of a new Ms scale and calibration function, termed Moscow-Prague formula, by Karnik et al. (1962):
for epicentral distances 2° < Δ < 160° and source depth h < 50 km. The IASPEI Committee on Magnitudes recommended at its Zürich meeting in 1967 the use of this formula as standard for Ms determination for shallow seismic events (h ≤ 50 km)
Work started by Gutenberg developed a magnitude scale based on surface wave recordings at teleseismic distances. The measure of amplitude is the maximum velocity (A/T)max. This allowed not only to link the scale to the energy, but also to account for the large variability of periods T corresponding to the maximum amplitude of surface waves, depending on distance and crustal structure.
Surface wave magnitude

## Slide 19
Gutenberg (1945b and c) developed a magnitude relationship for teleseismic body waves such as P, PP and S in the period range 0.5 s to 12 s. It is based on theoretical amplitude calculations corrected for geometric spreading and (only distance-dependent!) attenuation and then adjusted to empirical observations from shallow and deep-focus earthquakes, mostly in intermediate-period records:
  mB = log (A/T)max + Q(Δ, h)
Gutenberg and Richter (1956a) published a table with Q(Δ) values for P-, PP- and S-wave observations in vertical (V=Z) and horizontal (H) components for shallow shocks, complemented by diagrams Q(Δ, h) for PV, PPV and SH which enable also magnitude determinations for intermediate and deep earthquakes. These calibration functions are correct when ground displacement amplitudes are measured in intermediate-period records and given in micrometers (1 μm = 10-6 m).
Body wave magnitude

## Slide 22
  Later, with the introduction of the WWSSN short-period 1s-seismometers (see Fig. 3.11, type A2) it became common practice at the NEIC to use the calibration function Q(Δ, h) for short-period PV only. In addition, it was recommended that the largest amplitude be taken within the first few cycles (see Willmore, 1979) instead of measuring the maximum amplitude in the whole P-wave train. One should be aware that this practice was due to the focused interest on discriminating between earthquakes and underground nuclear explosions. The resulting short-period mb values strongly underestimated the body-wave magnitudes for mB > 5 and, as a consequence, overestimated the annual frequency of small earthquakes in the magnitude range of kt-explosions. Also, mb saturated much earlier than the original Gutenberg-Richter mB for intermediate-period body waves or Ms for long-period surface waves Therefore, the IASPEI Commission on Practice issued a revised recommendation in 1978 according to which the maximum P-wave amplitude for earthquakes of small to medium size should be measured within 20 s from the time of the first onset and for very large earthquakes even up to 60 s (see Willmore, 1979, p. 85). This somewhat reduced the discrepancy between mB and mb but in any event both are differently scaled to Ms and the short-period mb necessarily saturates earlier than medium-period mB.

## Slide 23
  However, some of the national and international agencies have only much later or not even now changed their practice of measuring (A/T)max for mb determination in a very limited time-window, e.g., the International Data Centre for the monitoring of the CTBTO still uses a time window of only 6 s (5.5s after the P onset), regardless of the event size.

## Slide 25
Why is it called “moment”?
Radiation from a shear dislocation with slip S over area A in material with rigidity μ is identical to that from a double couple with strength μ UA (units stress*displacement*area, but stress = force/area, so units = force*displacement = a couple = work = energy)

## Slide 26: Nomenclature
Mw
  Defined by Kanamori as an energy magnitude (includes a parameter in addition to moment), but he clearly had in mind the present mapping of moment and magnitude but setting the additional parameter to a constant value
M
  The first explicit mapping of moment (M0) and moment magnitude (M)
  Today people by-and-large use Mw (can write it in email); only purists such as DMB use M.

## Slide 27: What is the proper equation?
M = 2/3 log M0 – 10.7?
M = 2/3 log M0 – 10.73 ?
The former is correct, it corresponds to
Log M0 = 1.5M + 16.05 (not 16.0 or 16.1)
Hanks (personal commun.) chose 16.05 to average relations with constant terms of 16.0 and 16.1

## Slide 28: Why use moment magnitude?
It is the best single measure of overall earthquake size
It does not saturate (discussed later)
It can be estimated from geological observations
It can be estimated from paleoseismology studies
It can be tied to plate motions and recurrence relations

## Slide 29: Empirical relations can be used to estimate moment magnitude based on size of felt area – eg. Johnston et al., 1996 relations for mid-plate areas

## Slide 30
Moment Magnitude is the Best Measure of Earthquake Size

## Slide 31
“the big one”
Moment
Physical units (dyne-cm)
1026: Northridge, 1994
1030: Sumatra, 2004
Big range!
No saturation:
bigger rupture 
bigger moment

## Slide 32
The Largest Earthquakes
M is the appropriate choice for comparing the largest events, it does not saturate.
1960 Chile 9.5
2004 Sumatra 9.3
1964 Alaska 9.2
1952 Kamchatka 9.1
1965 Aleutians 9.0
(This pie chart needs to be revised to include the 2004 Sumatra earthquake, but the chart serves to emphasize that 0.1 M units corresponds to a factor of 1.4 increase in moment.)

## Slide 33
Why are the largest earthquakes along subduction zones?
For crustal earthquakes the width is limited by the thickness of the superficial crust brittle layer (~20 km). The thickness of the brittle layer is controlled by temperature, which increases with depth
Width is often considered smaller than the length even for small earthquake
ORDERS OF MAGNITUDE
Fault width

## Slide 34
20 km
surface
brittle
plastic
ORDERS OF MAGNITUDE
Fault width

## Slide 35
20 km
surface
brittle
plastic
faults
ORDERS OF MAGNITUDE
Fault width

## Slide 36
20 km
surface
brittle
plastic
faults
ORDERS OF MAGNITUDE
Fault width

## Slide 37: Converting between magnitude scales: Empirical relations (or sometimes theoretical relations) can be used to convert between magnitude scales. This is important in deriving magnitude recurrence statistics for a region or source zone, as all magnitudes should be first reported on the same scale before characterizing their statistics

## Slide 38: Surface wave magnitude is a close approximation to Moment M for Ms 6 to 8 events

## Slide 39: Body-wave magnitude is not a good measure of moment M, especially for large events

## Slide 40
Relations between magnitude scales

## Slide 41
Magnitude Discrepancies
Ideally, you want the same value of magnitude for any one earthquake from each scale you develop, i.e.
    MS = mb = ML = M
But this does not always happen:
  San Francisco 1906: MS = 8.3, M = 7.8
  Chile 1960: MS = 8.3, M = 9.6

## Slide 42: Why Don’t Magnitude Scales Agree?
Simplest Answer:
  Earthquakes are complicated physical phenomena that are not well described by a single number.
  Can a thunderstorm be well described by one number ? (No. It takes wind speed, rainfall, lightning strikes, spatial area, etc.)

## Slide 43: Why Don’t Magnitude Scales Agree?
More Complicated Answers:
    The distance correction for amplitudes depends on geology.
    Deep earthquakes do not generate large surface waves - MS is biased low for deep earthquakes.
    Some earthquakes last longer than others, even though the peak amplitude is the same.
    Variations in stress release along fault, for same moment.
    Not all earthquakes are self similar (that is, the relative radiation at different frequencies can differ--- examples: 1999 Chi-Chi compared to “standard” California earthquake).

## Slide 44: Why Don’t Magnitude Scales Agree?
Most complicated reason:
  Magnitude scales saturate
  This means there is an upper limit to magnitude no matter how “large” the earthquake is
  For instance Ms (surface wave magnitude) seldom gets above 8.2-8.3

## Slide 45
Example: mb “Saturation”
mb seldom gives values above 6.7 - it “saturates”.
mb must be measured in the first 5 seconds - that’s the (old) rule.

## Slide 46
What Causes Saturation?
The rupture process.
  Small earthquakes rupture small areas and are relatively depleted in long-period signals.
  Large earthquakes rupture large areas and are rich in long-period motions (we’ll study this later, when we discuss source scaling)

## Slide 47
What Causes Saturation?
The relative size of the fault and the wavelength of the motion used to determine the magnitude is a key part of the explanation.
Small fault compared to the wavelength: the magnitude will be a good measure of overall earthquake size.
Large fault compared to the wavelength: the magnitude will be determined by radiation from only a portion of the fault, and the magnitude will not be a good measure of overall fault size

## Slide 48
Saturation (cartoon)

## Slide 49
Relations between Magnitude Scales
Note saturation

## Slide 50: Are mb and Ms still useful?
YES!
  Many (most) earthquakes are small enough that saturation does not occur
  Empirical relations between energy release and mb and Ms exist
  The ratio of mb to Ms can indicate whether a given seismogram is from an earthquake or a nuclear explosion (verification seismology)

## Slide 51
(Whoops, this uses moment. Oh well, a plot of Ms vs. mb is similar)

## Slide 52
Magnitude Summary
Magnitude Symbol Wave Period
Local (Richter) ML S or Surface Wave* 0.8 s
Body-Wave mb P 1 s
Surface-Wave Ms Rayleigh 20 s
Moment Mw, M Rupture Area, Slip 100’s-1000’s
Magnitude is a measure of ground shaking amplitude.
More than one magnitude scale is used to study earthquakes.
All magnitude scales have the same logarithmic form.
Since different scales use different waves and different period vibrations, they do not always give the same value.

## Slide 53: Energy magnitude Me
Me = 2/3 (log Es – 4.4)
However, this ratio depends on the stress drop Δσ which varies by about three orders of magnitude
P. Bormann
For shallow EQs Choy and Boatwright (1995) found
Boatwright & Choy (1985)
Choy & Boatwright (1995)
with Me = Mw + 0.27
for Kanamori´s average condition:
Es/M0 = 5 X 10-5.
For some deep EQ´s Δσ up to about
100 MPa has been determined !

## Slide 54: Mw and Me may differ significantly !
• Mw is related to average displacement and rupture area and thus to
=> tectonic effects of EQ
Reprinted from Choy et al., 2001
P. Bormann
• Me is more closely related to the exitation of higher frequencies and thus to
=> damage potential of EQ

## Slide 55: Conclusions
P. Bormann
• Mw and Me are the only physically well-defined and non-saturating
magnitudes, however, they mean different things.
• Determination of Mw and Me has to be based on (V)BB, digital
records (bandwidth: 2 to 4 decades or 6 to 13 octaves).
• All classical band-limited magnitudes (typically 1 to 3 octaves),
saturate (e.g.; Ml, mb, mB and Ms).
• Band-limited magnitudes still form the largest magnitude data
set. They have merits on their own (e.g., Ml-I0, mb-Ms ratio, etc.).

## Slide 56
ORDERS OF MAGNITUDE
Seismic magnitude

## Slide 57: Magnitude-frequency distribution

## Slide 59: Recurrence Rate

## Slide 60: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: ? mm/yr

## Slide 61: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: 20 mm/year
Mmax = ?

## Slide 62: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: 20 mm/year
Mmax = 8, X = ?

## Slide 63: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: 20 mm/year
Mmax = 8, X = 6 m  Tr = ?

## Slide 64: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: 20 mm/year
Mmax = 8, X = 6 m  Tr = 6/(.02) = 300 yrs

## Slide 65: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: 20 mm/year
Mmax = 7.5, X = ?

## Slide 66: Slip Rate  Recurrence Rate
Slip rate = N mm/year
Mmax event = X meters (average) slip
Characteristic model: Tr = X/N
e.g
Sagaing fault: 20 mm/year
Mmax = 7.5, X = 3 m  Tr = ?

## Slide 67: Slip Rate  Recurrence Rate
Gutenberg-Richter distribution:
~10% of moment released in M<Mmax events
e.g
Sagaing fault: 20 mm/year
Mmax = 8, X = 6 m  Tr = 6/(.018) = 333 yrs
Mmax = 7.5, X = 3 m  Tr = 3/(.018) = 167 yrs

## Slide 68: If time remains, proceed to ROSE_2013_W1D4L1_Fourier_spectra.pptx

## Slide 69: End