## Slide 1
Rose School Lecture – 2013
S. Akkar and D. M. Boore
Fundamentals of Seismology & Seismic Hazard Assessment
MEASURES OF STRONG MOTION and PROCESSING OF DATA

## Slide 2: Ground-motion intensity measures (GMIMs) for engineering purposes
PGA, PGV
Response spectra (elastic, inelastic)
Others (Arias intensity (avg. spectra over freq.), power spectra, Fourier amplitude spectra, duration)
Time series

## Slide 3
Ground-Motion Intensity Measures (GMIMs) can be grouped into three categories:
Amplitude parameters
Frequency content parameters
Strong ground motion duration parameters
Some of these parameters can describe only one characteristic feature of a ground motion. While others may reflect two or three features at the same time.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 4
Amplitude parameters
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 5
Time series is the most common way of describing a ground motion. The time series of a ground motion can be
a
v
d
t
t
t
Acceleration: shows a significant proportion of relatively high frequencies.
Velocity: shows substantially less high frequency motion than the acceleration.
Displacement: dominated by relatively low frequency motion.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 6
Peak ground acceleration (PGA)
Largest absolute value of acceleration obtained from an accelerogram.
t
easy to measure because the response of most instruments is proportional to ground acceleration
liked by many engineers because it can be related to the force on a short-period building
convenient single number to enable rough evaluation of importance of records

## Slide 7: Peak ground acceleration (PGA)
BUT it is not a measure of the force on most buildings
and it is controlled by the high frequency content in the ground motion (i.e., it is not associated with a narrow range of frequencies); records can show isolated short-duration, high-amplitude spikes with little engineering significance
It is not associated with a specific frequency of ground shaking

## Slide 8: Peak ground velocity (PGV) (obtained from single integration of acceleration time series)
Many think it is better correlated with damage than other measures
It is sensitive to longer periods than PGA (making it potentially more predictable using deterministic models)
BUT it requires digital processing (no longer an important issue)

## Slide 9: Peak ground displacement (PGD) (obtained from double integration of acceleration time series)
The best parameter for displacement-based design?
BUT highly sensitive to the low-cut (high-pass) filter that needs to be applied to most records (in which case the derived PGD might not represent the true PGD, unlike PGA, for which the Earth imposes a natural limit to the frequency content). For this reason I recommend against the use of PGD.

## Slide 10
PGA and PGV can be used for a rapid response to picture the extent and variation of ground shaking throughout a well-instrumented, seismic-prone region.
Read PGAs and PGVs from the strong motion instruments
Use the relevant relations and derive intensities.
Draw these maps (ShakeMap) to portray the event
Courtsey of Dave Wald
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 11
Note that
  The maps should only serve for a rapid (preliminary) detection of the earthquake extent.
  One shortcoming of ShakeMaps is that they need a dense array for the computation of peak ground motion amplitudes. For regions where the instrumentation is scarce, the shake map is produced through ground-motion prediction equations (GMPEs) that should be chosen very carefully to reflect the seismicity of the region.
  These maps should be used with caution because of the large dispersion on the computed regression equations.
  For more information: http://www.shakemap.org
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 12
Frequency content parameters
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 13
The dynamic response of structural systems, facilities and soil is very sensitive to the frequency content of the ground motions.
The frequency content describes how the amplitude of a ground motion is distributed among different frequencies.
The frequency content strongly influences the effects of the motion. Thus, the characterization of the ground motion cannot be complete without considering its frequency content.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 14
Elastic response spectra (many structures can be idealized as SDOF oscillators)

## Slide 15
Dr. Sinan Akkar
k, c
m
represents the mass of the system
represents the mechanical properties of the system (stiffness).
represents the energy dissipation mostly due to friction, opening and closing of microcracks, friction between structural and nonstructural components etc (viscous damping coefficient).
ug
ut = ug + u
m
k
c
Relative displacement
Total displacement
Ground displacement
Single Degree of Freedom (SDOF) Harmonic Oscillator
Strong Ground Motion Parameters – Data Processing

## Slide 16
Dr. Sinan Akkar
Dynamic Equilibrium
internal force due to relative displacement u.
inertia force due to total acceleration acting on the mass m.
FS = ku
FI
FD
FS
m
FS + FD + FI = 0
FD = cu
.
internal force due to elative velocity acting on the viscous damping c.
FI = mut
..
Strong Ground Motion Parameters – Data Processing

## Slide 17
Dr. Sinan Akkar
For elastic systems:
u
k
mu + cu + ku = -mug
.
..
mu + cu + FS(u,u) = -mug
..
..
FS = ku
For inelastic systems:
u
F
FS = f(u,u)
.
..
.
Equation of motion
Equation of motion
.
F
Depends prior deformation history and whether deformation is currently increasing (u > 0) or decreasing (u < 0)
.
.
Strong Ground Motion Parameters – Data Processing

## Slide 18
Dr. Sinan Akkar
The equation of motion for an elastic system can be solved either analytically or numerically. However, there are very few cases in which the equation of an inelastic system can be solved analytically. The solutions for the inelastic case is usually numerical.
Nonlinear oscillator response is out of scope of this lecture
Strong Ground Motion Parameters – Data Processing

## Slide 19
Dr. Sinan Akkar
Critical damping,  and natural frequency n are the primary factors that effect the SDOF elastic response:
For a constant damping:
As the period of vibration grows, the oscillator response is dominated by the long period components of the ground motion.
Strong Ground Motion Parameters – Data Processing

## Slide 20
Important Asymptotic Cases (for which it is easy to solve the oscillator equation)

## Slide 21
Short-period oscillator response = PGA

## Slide 22
intermediate-period oscillator response not a relatively broadband motion PGA or PGD, but it is more oscillatory

## Slide 23
Long-period oscillator response = PGD (best seen by looking at the displacement response of the oscillator to the spectrum of ground displacement)

## Slide 24
. . . .
A plot of the absolute peak values of an elastic response quantity as a function of vibration period Tn of an SDOF system, or a related parameter such as circular frequency n or cyclic frequency fn. Each such plot is for a fixed damping ratio, .
1(T1)
2(T2)
3(T3)
n(Tn)
Elastic Response Spectrum

## Slide 26
At short periods, oscillator response proportional to base acceleration

## Slide 31
At long periods, oscillator response proportional to base displacement

## Slide 32
convert displacement spectrum into acceleration spectrum (multiply by (2π/T)2)--
Acceleration spectrum usually used in engineering

## Slide 33: Types of Response Spectra
SD: relative displacement response
PSA: pseudo-absolute response spectral acceleration
SA: absolute response spectral acceleration
PSV: pseudo-relative response spectral velocity
RV: relative response spectral velocity
Prefer PSA (simply related to SD, same ground-motion prediction equations can be used for SD and PSA)
See aa_pa_rv_pv_2.pdf on the Dave’s Notes page of my web site (www.daveboore.com) for details (but somewhat different notation)

## Slide 34
At short and very long periods, damping not significant (lin-lin and log-log plots to emphasize different periods of motion):

## Slide 35: Why is a RS Useful?
Buildings can be thought of as single-degree of freedom harmonic oscillators with a damping (nominally 5%) and free period (about 0.1 s per story)
A RS for a given record then gives the response of a building for the buildings resonant period and damping

## Slide 36
PGA generally a poor measure of ground-motion intensity. All of these time series have the same PGA:
(Could not show this before because the next slide, which is associated with this slide, uses response spectra, so I had to discuss that first)

## Slide 37
But the response spectra (and consequences for structures) are quite different (lin-lin and log-log plots to emphasize different periods of motion):

## Slide 39: Dealing with Two Horizontal Components
Treat each independently
Choose a random component
Compute vector sum of RS for each period
Compute geometric mean for each period
Compute GMRotI50
Compute RotD50 (and RotD00, RotD100)

## Slide 40: How RotDnn is Computed
Project the two as-recorded horizontal time series into azimuth Az
For each period, compute PSA, store Az, PSA pairs in an array
Increment Az by δα and repeat first two steps until Az=180
Sort array over PSA values
RotD50 is the median value
RotD00, RotD100 are the minimum and maximum values
NO geometric means are used

## Slide 42
To convert GMPEs using random component as the IM (essentially, the as-recorded geometric mean), multiply by RotD50/GM_AR
To convert GMPEs using GMRotI50 as the IM (e.g., 2008 NGA GMPEs), multiply by RotD50/GMRotI50

## Slide 44
Long-period motions are usually more coherent (linearly polarized) than short-period motions

## Slide 45
The RotD100 angle approaches a value of about 140° for periods longer than about 10 s, and because the motions are then close to being linearly polarized, the difference in angles for RotD100 and RotD00 is then about 90 °

## Slide 46: References
Boore, D. M., J. Watson-Lamprey, and N. A. Abrahamson (2006). Orientation-independent measures of ground motion, Bull. Seismol. Soc. Am. 96, 1502-1511.
Boore, D. M. (2010). Orientation-independent, non geometric-mean measures of seismic intensity from two horizontal components of motion, Bull. Seismol. Soc. Am. 100, 1830-1835.

## Slide 47
Duration parameters
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 48
Strong ground motion duration is related to the earthquake magnitude
Data from Guerrero, Mexico (Anderson and Quaas, 1988)
Courtesy of Prof. John Anderson, University of Nevada at Reno
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 49
Duration of strong ground motion plays an important role as amplitude and frequency content parameters in seismic hazard assessment
Ground motion duration
is important for the response of foundation materials as the build up of pore water pressure and essentially the liquefaction is strongly dependent on duration
is important for relatively weak and short period structures as their inelastic deformations are strongly dependent on duration (Mahin, 1980)
is important for any structure with stiffness and strength degrading characteristics
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 50
Definitions for strong motion duration
Bracketed durations (Db): Total time elapsed between the first and last excursions of a specified level of acceleration, ao.
Uniform durations (Du): Defined by a threshold level of acceleration, ao but not as an interval between the first and final peaks that exceed this level. It is the sum of the time intervals during which the acceleration is greater than the threshold.
Significant durations (Ds): based on the accumulation of energy in the accelerogram represented by the integral of the ground acceleration, velocity, or displacement. If integral is of ground acceleration then the quantity is related to Arias Intensity.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 51
Bracketed duration
Uniform duration
Significant duration
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 52
A well-known significant duration definition:
The interval between the times at which 5% and 95% of the total integral is attained (Trifunac and Brady, 1975) (currently, the 5%--75% duration seems to be used often).
5%AI
95%AI
AI
Bommer and Martinez-Pereíra, 1999
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 53
The bracketed, uniform and significant durations are based on the characteristics of the record. There are a few other durations that are based on the response of a specified structure (Structural response based).
Durations definitions that are based on ground motion characteristics are more relevant to seismic hazard assessment.
However
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 54
For EQUAL ACCELERATIONS, greater duration is generally more damaging.
For EQUAL ENERGY, shorter duration represents more hazard.
Thus
One should be very careful when defining the strong motion duration.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 55
Other strong ground-motion parameters
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 56
Root mean square (RMS) acceleration
reflects the effects of the amplitude and the frequency content of a strong motion record.
Ang (1990) described a “characteristic intensity” that is related linearly to structural damage due to maximum deformations and absorbed hysteretic energy.
Duration of the motion
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 57
Arias Intensity: based on the integral of squared acceleration over time (“Husid” plots, shown in previous slides).

## Slide 58
Cumulative absolute velocity
The cumulative absolute velocity has been found to correlate well with the structural damage potential.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing
(Kramer, 1996)
Definition of CAV according to Reed and Kennedy (1985):
Average value of the absolute value of acceleration during 1 sec time windows that include an acceleration of 0.025g or larger, multiplied by the total duration of the 1-sec time windows. Reed and Kennedy (1985) recommended that if CAV < 0.016g-sec, the ground motion will not be potentially damaging to engineered structures.

## Slide 59
Characterization of ground motions as well as seismic demand have been developed primarily from recordings obtained from strong-motion accelerographs.
STRONG MOTION DATA PROCESSING
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing
Primary Processing Operations:
Baseline Correction
High-pass filtering

## Slide 60
The global databank of strong-motion accelerographs that has been accumulated since the first records were obtained in Long Beach, California, has been of prime importance to the development of earthquake engineering. (As of the end of 1980 there were about 1700 accelerographs in the US - 1350 of those in California-, and by January of 1982 over 1400 accelerographs in Japan).
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 61
For a variety of reasons digitized strong-motion data contain noise (extraneous motions). For engineering uses of strong-motion data it is important to be able to estimate the level of noise present in each accelerogram and the degree to which this may affect different parameters that are derived from the records.
Main parameters of interest for engineering applications are
  ordinates of response spectra both for acceleration and displacement
  peak ground motion values (i.e. peak ground acceleration, velocity and displacement)
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 62
Analog accelerographs
Three important disadvantages of analog accelerographs:
Always triggered by a specified threshold of acceleration which means the first motions are often not recorded
The limitation of natural frequency of analog instruments. They are generally limited to about 25 Hz.
It is necessary to digitize the traces of analog instruments as they record on film or paper (most important disadvantage as it is the prime source of noise)
These instruments produce traces of the ground acceleration against time on film or paper. Most widely used analog instrument is the Kinemeterics SMA-1
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 63
Digital accelerographs
Digital accelerographs came into operation almost 50 years after the first analog strong motion recorders. Digital instruments provide a solution to the three disadvantages associated with the earlier accelerographs:
1. They operate continuously and by use of pre-event memory are able to retain the first wave arrivals.
2. Their dynamic range is much wider, the transducers having natural frequencies of 50 to 100 Hz or even higher
3. Analog-to-digital conversion is performed within the instrument, thus obviating the need to digitize the records.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 64
Noise characteristics of strong-motion data
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 65
It is important for strong-ground motion users to appreciate that digitized accelerograms are never pure.
The purpose of processing accelerograms is to optimize the balance between acceptable signal-to-noise ratios and the information required for a particular application both of which depend on period or frequency.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 66
Analog accelerograms
The problems of noise in the analog record are generally not apparent from acceleration time-history. The most important effects of noise in the record only become apparent when the acceleration trace is integrated to obtain velocity and displacement time series
The velocity and displacements obtained from integration of accelerogram will generally appear unphysical: the ground motion appears as a single asymmetrical elastic displacement pulse of more than 2 m amplitude.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 67
A problem encountered with some digitized analogue records is shifts in the baseline. (Result of the record being digitized in sections and not being correctly spliced)
The procedure to compensate for their effect is essentially the same for both analog and digital recordings; these are described in the succeeding slides
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 68
The unphysical nature of the velocities and displacements obtained from integration are mostly the unknown baseline and long-period noise coming from variety of sources but predominantly from the imperfection of tracking in digitizers (Trifunac et al., 1973; Hudson, 1979; Trifunac and Todorovska, 2001). Long period error can also be introduced by lateral movements of the film during recording and warping of the analog record prior to digitization.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 69
It is not possible to identify, separate and remove the noise in order to recover the actual seismic signal.
The best that can be achieved is
  Identify those portions of the frequency content of the record where the signal-to-noise ratio is unacceptably low .
  Remove the contaminated frequencies from the record through processing.
Thus, we are not “correcting” the raw data but we are retrieving the most useful information through a suitable processing.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 70
Most analog accelerographs produce fixed traces
on the film together with the actual traces of motion. These fixed traces can (if digitized) can model the noise.
Unfortunately, the fixed traces are very often not digitized or else the digitized fixed traces are not kept. Hence it is rare that a model of the noise can be obtained from this information.
Shakal et al. (1984), Lee and Trifunac (1984) and Skarlatoudis et al. (2003) have examined the noise from fixed traces. Although they provide useful information these studies correspond to a particular combination of accelerograph and digitizer.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 71
Digital accelerograms
Digital accelerographs are superior then the analog accelerographs. They have improved dynamic range, higher sampling rate and there is no need of digitization process. However, the need to apply processing to the records is not entirely eliminated, as can be seen in the next figure.
The nature of baseline errors in digital recordings is distinct from those in digitized analog recordings. One advantage of digital recordings is that presence of the pre-event memory portion of the recordings. It provides a direct model for the noise in the record. However, in digital records the noise is actually associated with the signal itself, hence the pre-event memory is not a incomplete model for the noise.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 72
the true baseline of the digital record is still unknown and this manifests in the velocity and displacement time-histories obtained by double integration.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 73
High-frequency noise and instrument effects
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 74
Standard vs. non-standard noise
In many records, errors are found that are not from the characteristics of the instrument . These are non-standard errors and should be removed prior to routine processing.
An example of non-standard error: spurious “spikes” in the digitized record can be identified at about 10.5, 16 and 26 seconds
Fix by: replacing the acceleration ordinate of the spike with the mean of the accelerations of the data points either side.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 75
Spectral acceleration of the record shown in slide 14 before and after removing the spikes.
Spikes clearly constituted a serious noise contamination at short periods but it is also noted that their elimination appears to have led to the removal of a small part of the signal at longer periods.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 76
Limited transducer frequency and digitization process itself introduce high frequency noise in analog instruments
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 77
The effect of applying a correction for the instrument characteristics results in a slight increase in the amplitudes at frequencies greater than 30 Hz. This will affect the demands on very stiff structures that are of little relevance in daily design practice
Hard rock recording at a distance of 4km from the source (as is)
Same record corrected for instrument response
Theoretical instrument response
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 78
High frequency records attenuate very fast as the site gets softer and distance to source increases. This fact decreases the importance of high frequency motions in many cases.
Two records from the same event recorded at different stations. Gray one is recorded at a distance of 26 km. The black solid curve is recorded at a distance of 31 km.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 79
Corrections for transducer characteristics
For digital recordings, instrument corrections should not be necessary. For analog recordings, if the engineering application is concerned with motions at frequencies above 20 Hz and the site characteristics are sufficiently stiff for appreciable amplitudes at such frequencies to be expected, a correction should be considered.
Instrument corrections amplify the high-frequency motions. Therefore they should be done carefully in order not to amplify the high frequency noise
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 80
Techniques more widely used in current practice generally perform the correction by using either higher-order approximations to the derivatives or using frequency-domain corrections (e.g., Shyam Sunder and Connor, 1982; Converse and Brady, 1992).
If it is judged that there is significant high-frequency noise in the record this can be removed by the application of high-cut (low-pass) filters.
Correction procedures for transducer characteristics
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 81
Baseline adjustments
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 82
A major problem encountered with both analog and digital accelerograms are distortions and shifts of the baseline, which result in unphysical velocities, displacements, and long-period response spectra.
One approach to compensating for these problems is to use baseline adjustments, whereby one or more baselines, which may be straight lines or low-order polynomials, are subtracted from the acceleration trace.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 83
Multi-segment baselines
Application of a piece-wise sequential fitting of baselines to the velocity trace. There are clearly identifiable offsets in the baseline. A similar procedure could be applied directly to the acceleration time-history (the derivative of the baseline fits to velocity is simultaneously subtracted from the acceleration time series).
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 84
Baselines to remove long-period noise
The distortion of the baseline encountered in digitized analog accelerograms is generally interpreted as being the result of long-period noise combined with the signal.
Baselines can be used as a tool to remove at least part of this noise – and probably some of the signal with it – as a means of recovering less unphysical velocities and displacements.
There are many procedures that can be applied to fit the baselines, including polynomials of different orders.
A point that is worth making clearly is that in effect baseline adjustments are low-cut filters of unknown frequency characteristics.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 85
Physical rationale for baseline correction procedures
The ground velocity must return to zero the end of the ground shaking. This is indeed a criterion by which to judge the efficacy of the record processing. The final displacement, however, need not be zero since the ground can undergo permanent deformation either through the plastic response of near-surface materials or through the co-seismic slip on the fault (fling step). Fling step is observed at stations close to the fault rupture (when M ~ 6.5 and above). This displacement can be on the order of tens or hundreds of centimeters.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 86
Two approaches to fitting baselines to the velocity trace, and the changes that they impose on the acceleration trace.
One scheme is a simple quadratic fit to the velocity, a simplification of the more complex scheme proposed by Graizer (1979) in which a series of progressively higher-order polynomials are fit to the velocity trace.
Quadratic fit to velocity
Corresponding straight line for acceleration time series
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 87
The other approach approximates the complex set of baseline shifts with two shifts, one between times of t1 and t2, and one after time t2. The adjustment scheme can be applied to any record, with the advantage that the velocity will oscillate around zero (a physical constraint), but the scheme requires selection of the times t1 and t2.
Two alternative choices for t2
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 88
Determination of t1 and t2:
Iwan et al. (1985), the original proponents of the method, suggeted t1 and t2 as the times that correspond to the first and last exceedance of 50 m/s2. Alternatively, Iwan et al. (1985) proposed that t2 be chosen so as to minimize the final ground displacement.
Boore (2001) proposed t1 and t2 be any value provided that t1 > t2 and t2 is less than the total length of the record.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 89
Without a physical reason for choosing these times, the choices of t1 and t2 become arbitrary, and as illustrated in the figure, the long-period response spectrum ordinates are sensitive to the choice of t2 (t1 was not varied in this illustration). However, the sensitivity of spectral displacements starts for T > 10s.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 90
Residual displacements
Different t2 values result in significant variation in residual displacements
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 91
Boore proposed a further simplification to the baseline correction procedure originally proposed by Iwan et al. (1985).
He assumed that t1 = t2; there was only one baseline offset and that it occurred at a single time. The time is computed by the zero intercept of a line fit to the final part of the velocity trace.
This method is called as “v0” correction by the proponent of the procedure (Boore, 2001).
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 92
Filters to reduce low-frequency noise
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 93
Most widely used tool for reducing the long-period noise in accelerograms is the low-cut filter (Trifunac, 1971). Figure shows the raw and filtered accelerograms of an analog and digital recording. (Note different y-axis scales for displacement)
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 94
Choice of filtering technique
A wide range of filters to choose from: including Ormsby, elliptical, Butterworth, Chebychev and Bessel.
The correct application of the chosen filter is much more important than the choice of a particular filter.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 95
Terminology:
Low-cut filtering: removes the low-frequency (long-period) components of ground motion (also known as high-pass filtering)
High-cut filtering: removes the high-frequency (short-period) components of ground motion (also known as low-pass filtering)
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 96
Low-cut Butterworth filter with different filter orders for a cut off frequency of 0.05 Hz (20 seconds).
The filters are defined by a filter frequency and an order: the higher the order of the filter, the more rapid the roll-off.
roll-off
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 97
The fundamental choice of filtering is between causal and acausal filters.
Acausal filters: They do not produce phase distortion in the signal.
Causal filters: They result in phase shifts in the record.
The zero-phase shift of acausal filters is achieved in the time domain by passing the transform of the filter along the record from start to finish and then reversing the order and passing the filter from the end of the record to the beginning. To achieve the zero phase shift, acausal filters have to start acting prior to the beginning of the record. For this, they need zero pads before and after the record.
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 98
Even if there are pre- and post-event memory on digital recordings, you have to pad them with additional zeros if the required length of the filter pads are longer than the pre- and post-event portions of the record.
The length of the pads depends on the filter frequency and the filter order. (pads are needed regardless of whether the filtering is done in the time- or frequency-domain)
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 99
Application of causal and acausal filters, even with very similar filter parameters produce very different results in terms of the integrated displacements (shown above) and the elastic spectral response ordinates (shown in the next slide).
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 100
In case of causally filtered data: both elastic and inelastic response spectra can be sensitive to the choice of filter corner periods even for oscillator periods much shorter than the filter corner periods.
Ratio of 5%-damped pseudo absolute acceleration spectra (in cm/s2) for causal (top) and acausal (bottom) filtering, using the results for a filter corner of 100 s as reference.
causal
acausal
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 101
When acausal filters are applied, the pads are a tool of convenience but their retention as part of the processed record is important. If pads of acausally filtered data are not retained, the filtering effects will not be completely captured, as a portion of the filter transient will be removed.
An important remark regarding consistency of acceleration time series and ground-motion measures obtained from the acceleration time series
Dr. Sinan Akkar
Strong Ground Motion Parameters – Data Processing

## Slide 102
Note very small filter transients
Data from analog strong-motion accelerograph at station Dinar-Meteorology Station (RHYP=5 km,VS30=198 m/s) from the 01 October 1995 Dinar, Turkey, earthquake (M 6.4)

## Slide 103
Computing ground-motion intensity measure from pad-stripped data can lead to inconsistencies between ground-motion intensity measures (GMIMs) computed from the padded and filtered acceleration time series and from that time series after removing the seemingly unimportant padded portions

## Slide 104
Computing ground-motion intensity measure from pad-stripped data can lead to errors, particularly at long periods
See Boore, D. M., A. Azari Sisi, and S. Akkar (2012). Using pad-stripped acausally filtered strong-motion data,
Bull. Seismol. Soc. Am. 102, 751-760, for more information and other references.

## Slide 105: Choosing Filter Corners
Choosing filter corners often guided by
  Shape of Fourier acceleration spectrum (look for f2 slope)
  Appearance of displacement waveforms (do they “look reasonable”?)

## Slide 106
This is an example of how filter corners might be chosen on the appearance of the displacement time series

## Slide 109
Discuss highest usable period (important for GMPE development)
In spite of large differences in waveforms, the response spectra at periods of engineering interest are similar. Two general conclusions to be made here:
  Filtering alone is often all that is needed
  Response spectra at periods of engineering interest are often insensitive to filter cutoff periods for modern digital records

## Slide 110: A Case Study
TCU068 Recording, 1999 Chi-Chi (M 7.6) Earthquake

## Slide 112
TCU068

## Slide 118
gps vector similar to that from residual displacements obtained from the v0 baseline correction

## Slide 130
It’s time to forget work and go have some fun!
Tifosi may recognize
my maglia rosa as
that of the 1984
Giro d’Italia
winner Francesco
Moser

## Slide 131: END