## Slide 1
FUNDAMENTALS of ENGINEERING SEISMOLOGY
    SOURCE, PATH, AND SITE EFFECTS FROM OBSERVATIONS

## Slide 2: Overview of lecture
Properties of Data from Observations
  Data distribution in M-D space
  Path dependence of ground motion
  Magnitude dependence of ground motion
  Site dependence of ground motion
Acknowledgment: a number of slides are from G. Cultrera and A. Herrero

## Slide 3
The release of the accumulated elastic strain energy by the sudden rupture of the fault is the cause of the earthquake shaking

## Slide 4
Ground Motion Deconvolution
(Steidl)

## Slide 5
Seismic shaking in range of resonant frequencies of structures
Shaking often strongest on horizontal component:
  Earthquakes radiate larger S waves than P waves
  Decreasing seismic velocities near Earth’s surface produce refraction of the incoming waves toward the vertical, so that the ground motion for S waves is primarily in the horizontal direction
Buildings generally are weakest for horizontal shaking
Horizontal S and surface waves are most important for engineering seismology:

## Slide 6: Frequencies of ground-motion for engineering purposes
10 Hz --- 10 sec (usually less than about 3 sec)
Resonant period of typical N story structure ~ N/10 sec
  What is the resonant period of the building in which we are located?
Corner periods for M 5, 6, and 7 ~ 1, 3, and 9 sec

## Slide 8: Reminder: Play Chuettsu and Tottori movies (again)

## Slide 9
http://www.k-net.bosai.go.jp
1000 digital instruments installed after the Kobe earthquake of 1995
free field stations with an average spacing of 25 km
velocity profile of each station up to 20 m by downhole measurement
data are transmitted to the Control Center and released on Internet in 3-4 hours after the event
INSTRUMENTATION
Kyoshin Net: Japanese strong motion network

## Slide 10
Chuetsu

## Slide 11
Tottori

## Slide 12: Characteristics of Data
Magnitude-distance distribution depends on region
Change of amplitude with distance for fixed magnitude
Change of amplitude with magnitude after removing distance dependence
Site dependence
Scatter

## Slide 13: Distance Measures

## Slide 14
Observed data adequate for regression except
close to large ‘quakes
(the recently developed NGA database contains such records, primarily from Taiwan and Turkey)
Observed data not adequate for regression, use simulated data

## Slide 15
Updated M-R plots, using data from the PEER NGA-West2 2013 flatfile

## Slide 16: NGA-West2 PSAs (adjusted to Vs30=760 m/s) vs. RRUP
Notes: Next: site amp w BA w SM. Compare w iCB results.
Resi v vs30.
Filter, gmx SM.
Thursday, updates to ppt.
Linear term in gmpe that data sets. C term set by data in regression. Nonlin taken out.
BA c term not diff than gmpe work olmali.

## Slide 17: What do the data tell us about magnitude and path scaling?
There is significant scatter in the data. The scatter is larger for small earthquakes and generally increases with distance (at least to distances of about 200 km). In spite of the scatter, however, there are systematic distance and magnitude trends in the data, as discussed in the next items.
For a single magnitude and for all periods the motions tend to saturate for large earthquakes, that is, they approach a constant value, as the distance from the fault rupture to the observation point decreases. This can only be concluded definitively for large magnitudes, for which the rupture approaches the ground surface and therefore the distance measure used in in the figure can approach 0.0. Smaller earthquakes do not reach the surface, and therefore surface observations cannot be used to infer whether or not the motions near the rupture surfaces of small earthquakes saturate.

## Slide 18: What do the data tell us about magnitude and path scaling?
At any fixed distance the ground motion increases with magnitude in a nonlinear fashion, with a tendency to saturate for large magnitudes, particularly for shorter period motions. The overall magnitude scaling increases with increasing period, but it is smaller at short distances than at longer distances. For short periods and close distances there appears to be almost complete saturation for the motions from large earthquakes.
For a given period and magnitude the median ground motions decay with distance; this decay shows curvature at greater distances on the log-log plot used in the figure. This decay can be parameterized as exp(-αRRUP)/RRUPβ, where the terms in the numerator and denominator are similar to the decay from a point source due to anelastic attenuation and geometrical spreading, respectively. In log-log plots, the anelastic attenuation produces the curvature at greater distances, and the geometrical spreading produces the linear decay at closer distances. Careful inspection of the figure shows that the apparent geometrical spreading decreases as magnitude increases.

## Slide 19
Chi-Chi data are low at short periods
(note also scatter, distance dependence)
Illustrating distance and magnitude dependence

## Slide 20
And so are Denali and Kocaeli (or is Northridge high?)

## Slide 21: Scaling with magnitude

## Slide 25
Magnitude scaling
Note that each symbol represents the average of the strong-motion recordings for a single earthquake, correcting for the distance dependence.

## Slide 26: Path effects
Wave types
  Body (P, S)
  Surface (Love, Rayleigh)
Amplitude changes due to wave propagation
  Geometrical spreading (1/r in uniform media, more rapid decay for velocity increasing with depth)
  Critical angle reflections
  Waveguide effects
Amplitude changes due to intrinsic attenuation (conversion to heat) and scattering attenuation

## Slide 27
FAR SOURCE
far field, reflection and refraction
Reflection and refraction of a longitudinal (P) wave in an earthquake after it hits a boundary between two types of rock. Note conversion from P to S (angles determined by Snell’s law)
Picture of the paths of seismic P or S waves being reflected and refracted in rock structures of the Earth's crust.

## Slide 28
FAR SOURCE
Main crustal phases

## Slide 29: How does the motion depend on distance?
Generally, it will decrease (attenuate) with distance
But wave propagation in a layered earth predicts more complicated behavior (e.g., increase at some distances due to critical angle reflections (“Moho-bounce”)
Equations assume average over various crustal structures

## Slide 30
More distant data show limitations of function fit to closer data (but ground motions at greater distances are of little engineering interest)
From V. Graizer

## Slide 34
REFLECTION AND TRANSMISSION OF SEISMIC WAVES AT DISCRETE INTERFACES REDUCE THEIR AMPLITUDES.
FOUR OTHER PROCESSES ALSO REDUCE WAVE AMPLITUDES:
- GEOMETRICAL SPREADING
SCATTERING
MULTIPATHING
ANELASTICITY
THE FIRST THREE ARE ELASTIC PROCESSES, IN WHICH
THE ENERGY IN THE PROPAGATING WAVE FIELD IS CONSERVED.
IN CONTRAST, ANELASTICITY, SOMETIMES CALLED INTRINSIC ATTENUATION, INVOLVES CONVERSION OF SEISMIC ENERGY TO HEAT.
ATTENUATION
Definition

## Slide 35
2) Scattering: light dims as it is scattered by air molecules, dust, and water in the air. Scattering results when objects acting as Huygens' sources scatter energy in all directions. This effect is dramatic on a foggy night because scattered light causes a halo around the lamp.
1) Geometric spreading: light moves outward from lamp in expanding spherical wave fronts. By conservation of energy, the energy in a unit area of the growing wave front decreases as r-2, where r is the radius of the sphere or distance from the lamp.
ATTENUATION
Analogous behaviors for light

## Slide 36
Wave propagation produces changes of amplitude (not shown here) and increased duration with distance. Not included in these simulations is the effect of scattering, which adds more increases in duration and smooths over some of the amplitude changes (as does combining propagation over various profiles with laterally changing velocity)
Amplitude of each trace normalzed independently—cannot see geometrical spreading effects

## Slide 37
3) Light is focused or defocused by changes in the refractive properties of the air. This process causes mirages, where light is refracted differently by hot air just above the ground.
Similarly the distorted appearance of the setting sun results from seeing different parts of it through different levels of the atmosphere which refract light differently because of the vertical density gradient.
This effect is termed multipathing in seismology.
4) Some light energy is absorbed by the air and converted to heat. This process differs from the other three in that light energy is actually lost, not just moved onto a different path. It is called in seismology attenuation.
ATTENUATION
Analogous behaviors for light

## Slide 38
ALL FOUR PROCESSES ARE IMPORTANT FOR SEISMIC WAVES.
The first three are described by elastic wave theory, and can increase or decrease an arrival's amplitude by shifting energy within the wave field.
In contrast, anelasticity only reduces wave amplitudes because energy is lost from the elastic waves.
So much of seismology is built upon the approximation that the earth responds elastically during seismic propagation that it is easy to forget that the earth is not
perfectly elastic.
However, without anelasticity seismic waves from every earthquake that ever occurred would still be reverberating until the accumulating reverberations shattered the earth.
Elasticity is a good approximation for the earth's response to seismic waves, but there are many important implications and applications of anelasticity.
ATTENUATION
Definition

## Slide 39
For body waves, consider a spherical wavefront moving away from a deep earthquake. Energy is conserved on the expanding spherical wavefront whose area is 4 π r 2, where r is the radius of the wavefront.
Thus the energy per unit wave front decays as 1 / r2, and the amplitude decreases as 1 / r
GEOMETRICAL SPREADING
Body waves
Energy proportionnal to
Planar wave: Constant
Cylindrical wave :
Spherical wave:

## Slide 40
GEOMETRICAL SPREADING
Surface waves
Conical waves decay in

## Slide 41
Expect minimum at =90º, and maxima at 0º and 180º
GEOMETRICAL SPREADING
Surface waves

## Slide 42
From geometric spreading alone, expect minimum at =90º, and maxima at 0º and 180º
Also have effects of anelasticity
GEOMETRICAL SPREADING
Surface waves

## Slide 43
Seismic waves are focused and defocused by lateral variations in velocity.
Although physically this process is the same as the effects of vertical variations, it is often distinguished by the term multipathing.
The distinction reflects our view of the earth as an essentially layered planet with secondary lateral variations.
ATTENUATION
Multipathing

## Slide 44
MULTIPATHING
Focusing and defocusing

## Slide 45
TRACE RAY PATHS USING SNELL’S LAW
RAYS BEND AS WATER DEPTH CHANGES
FIND WHEN WAVES ARRIVE AT DIFFERENT PLACES
DENSITY OF WAVES SHOWS FOCUSING & DEFOCUSING
MULTIPATHING
Focusing and defocusing

## Slide 48
The unscattered wave travels the shortest distance and gives the initial arrival. Scattered energy lost from this arrival arrives later & could have been scattered from an infinite number of locations that yield the observed travel time. In a constant-velocity medium, the locus of possible scatterers is an ellipsoid with the source and receiver as foci. Larger ellipsoids define the possible scatterers for energy that arrives later.
SCATTERING
Seismic waves

## Slide 49
SCATTERING
Earth versus Moon

## Slide 50
a = size of heterogeneity; L = distance wave travels;  = wavelength
When the heterogeneity is large compared to the wavelength, we regard the wave as following a distinct ray path possibly distorted by multipathing.
When velocity heterogeneities are close in size to the wavelength, we think of scattered energy rather than distinct ray paths.
When heterogeneities are << than the wavelength, they simply change the medium's overall properties. The further the wave travels in the heterogeneous region, the more useful the scattering description becomes. Hence for longer distances, the wavelength range viewed as scattering increases.
ATTENUATION
Multipathing or scattering ?

## Slide 52
ANELASTICITY
Analogy with a damped oscillator

## Slide 53
ANELASTICITY
Wave amplitude with time

## Slide 54
Q and Q-1
The solution for the damped harmonic oscillator incorporated the damping through the quality factor Q.
Attenuation for seismic waves and a variety of other physical phenomena are often discussed in terms of Q or Q -1.
Q -1 has the advantage that is directly rather than inversely proportional to the damping.
No attenuation -> Q = ∞ 1/Q =0
High attenuation -> Q low 1/Q high
ANELASTICITY
Effect in the frequency domain

## Slide 55
Q > 10,000 in the cold and rigid subducting slab but is less than 75 beneath the hot back-arc basin.
ANELASTICITY
Variations of Q

## Slide 56
ANELASTICITY
Variations of Q

## Slide 57
Seismograms from an earthquake in Texas
recorded in Nevada and Missouri.
The MNV record has less high frequency energy
because the tectonically-active western U.S.
is more attenuating than the stable mid-continent.
ANELASTICITY
Effect on waveform at regional scale

## Slide 58
ANELASTICITY
Effect on waveform at regional scale

## Slide 59: Path-independent filtering of high frequencies
Fmax? (Hanks)
Kappa? (Anderson & Hough)
Site or source effect? Does it matter (perhaps, if the parameter controlling the high frequency filtering is magnitude dependent, as it might be if a source effect)

## Slide 60
Two alternate parameters to control the reduction of high frequencies are fmax and κ (these parameters appear in functions that have the effect of filtering out the high frequencies)

## Slide 61
But the most-used factor to describe this ‘extra’ attenuation was given by Anderson & Hough (1984):
the spectral decay parameter… κ:
(holds for frequency-independent Qef)
lin
(From O. Ktenidou)

## Slide 62
Plot κ against distance (each point corresponding either to a separate record at the same station, or separate recordings for the same earthquake), fit a line to the points. The zero-distance intercept is known as κ0. The part that depends on distance is accounted for by the Q parameter discussed in the path effects section.

## Slide 63
The attenuation controlled by both parameters is independent of the source-to-site distance. Here is a cartoon suggesting how this can be true:

## Slide 64
FMAX or κ
Origin
surface
OR
It exists a minimum size for the asperities of the fault
Anderson & Hough (1984)
Aki’s school

## Slide 65
f
ANELASTICITY
Effect in the frequency domain
Source convolved with high-frequency diminution

## Slide 66: Site Effects, Basin Waves,Spatial Variability, Azimuthal Dependence

## Slide 67: Basin Waves: Path effect or site effect?

## Slide 71
People have known for a long time that
motions on soil are greater than on rock
e.g., Daniel Drake (1815) on the 1811-1812 New Madrid sequence:
  "The convulsion was greater along the Mississippi, as well as along the Ohio, than in the uplands. The strata in both valleys are loose. The more tenacious layers of clay and loam spread over the adjoining hills … suffered but little derangement."

## Slide 72
Steidl

## Slide 73
Steidl

## Slide 74
Site Classifications for Use With
Ground-Motion Prediction Equations
Rock = less than 5m soil over “granite”, “limestone”, etc.
Soil= everything else
2. NEHRP Site Classes (based on VS30)
3. Continuous Variable (VS30)
1. Rock/Soil
620 m/s = typical rock
310 m/s = typical soil

## Slide 75
Time-averaged shear-wave velocity to depth z:
Average shear-wave slowness to depth z:

## Slide 77: Why VS30?
Most data available when the idea of using average Vs was developed were from 30 m holes, the average depth that could be drilled in one day
Better would be Vsz, where z corresponds to a quarter-wavelength for the period of interest, but
Few observations of Vs are available for greater depths
Vsz correlates quite well with Vs30 for a wide range of z greater than 30 m (see previous slide, from Boore et al., BSSA, 2011, pp. 3046—3059)

## Slide 78
VS30 as continuous variable
Note period dependence of site response

## Slide 79
Simplest: Rock vs Soil
(E. Field)
Notes: 1994 was about the time the SCEC Phase III effort began
Also the year of the Northridge earthquake, which was part of the impetus for the phase III study.

## Slide 80
2002 M 7.9 Denali Fault

## Slide 81
Site Classes are based on the average shear-wave velocity in the upper 30 m (discussed later).

## Slide 83
pulses 1 & 2: subevent 1
pulse 3: subevent 2
pulse 4: subevent 3
Remove high frequency by filtering to emphasize similarity of longer-period waveforms

## Slide 86
Site Amplification from global database (NGA-West2):

## Slide 87
Observations from global database (NGA-West2) can be modeled as:
or
with the results:

## Slide 88
"It is an easy matter to select two stations within 1,000 feet of each other where the average range of horizontal motion at the one station shall be five times, and even ten times, greater than it is at the other”
John Milne, (1898, Seismology)
Spatial Variability

## Slide 90
Comparing the 1966 and 2004 Aftershocks
Both Earthquakes Ruptured the Same Segment

## Slide 91
But with Some Important Differences

## Slide 92
Most Extensively Observed Earthquake to Date in the Near-Fault
Region

## Slide 94
Potential Contributing Factors to the Observed Ground Motion
Site conditions
Rupture propagation
Stopping phases
Prestress (“Asperities”)
Fault geometry

## Slide 99
A key concept in this course is the relation of frequency content of ground motion to such things as scaling with magnitude, attenuation with distance, and the effect of local site geology. In general things become more complex as frequency increases, leading to differences in deterministic and stochastic predictions of ground shaking.

## Slide 101
Azimuth-dependent amplification of weak and
strong ground motions within a fault zone
(Nocera Umbra, central Italy)
G. Cultrera, A. Rovelli, G. Mele, R. Azzara,
A. Caserta, and F. Marra (2003)

## Slide 105
CONTINUE WITH PINGTUNG

## Slide 106
REFLECTION AND TRANSMISSION OF SEISMIC WAVES AT DISCRETE INTERFACES REDUCE THEIR AMPLITUDES.
FOUR OTHER PROCESSES ALSO REDUCE WAVE AMPLITUDES:
- GEOMETRICAL SPREADING
SCATTERING
MULTIPATHING
ANELASTICITY
THE FIRST THREE ARE ELASTIC PROCESSES, IN WHICH
THE ENERGY IN THE PROPAGATING WAVE FIELD IS CONSERVED.
IN CONTRAST, ANELASTICITY, SOMETIMES CALLED INTRINSIC ATTENUATION, INVOLVES CONVERSION OF SEISMIC ENERGY TO HEAT.
ATTENUATION
Definition